## Slide 1
SEATEMP
instrument
calibration
Data variable
INST A
calibrations
installations
From day 1-3, the variable SEATEMP is measured by instrument A (instrument instance A). The instrument was commissioned on date 1 (date_valid_from)
seatemp:instrument = "/instruments/INST_A" ;
INSTALLATION A
Instrument A was installed on date 1 (date_valid_from) in position X, Y, Z. date_valid_to will be populated when instrument A is uninstalled
CAL A
instrument A has a manufacturer calibration A.
Calibration A is good between dates 1 and 2 (valid dates to/from). For example, Date 2 might be when the sensor is expected to be sent for calibration.
If calibration A is applied to SEATEMP, then it is linked in the calibration attribute . This would be true for the SBE38 for example. This would not be true for the PAR sensors.
seatemp:calibration = "/calibrations/CAL_A" ;
INST B
calibrations
installations
INSTALLATION B
During day 3, the instrument A was changed to instrument B (instrument instance B)
seatemp:instrument = "/instruments/INST_A, "/instruments/INST_B" ;
date_valid_to was populated in installation A
On day 4, inst A, installation A, cal A will not appear in daily file
seatemp:instrument = "/instruments/INST_B" ;
Instrument B was installed on date 1 (date_valid_from) in position X, Y, Z.
CAL B
instrument B has a manufacturer calibration B etc.
1
2
3
4
5
6
7
If calibration B is applied to SEATEMP, then it is linked in the calibration attribute alongside calibration A on day 3 but not on day 4
Day 3:
seatemp:calibration = "/calibrations/CAL_A,/calibrations/CAL_B" ;
Day 4:
seatemp:calibration = /calibrations/CAL_B" ;
8
Group instruments
Group installations
Group calibrations
INSTALLATION C
On day 6, instrument B changed position to installation C.
9
13
CAL C
After the cruise a scientist or data manager applied a calibration after comparing SEATEMP to the CTD temperature. It was only valid from dates 1 and 2 during the cruise (date_valid_from/to)
seatemp:calibration = /calibrations/CAL_B,/calibrations/CAL_C/" ;
PPAR_OUTPUT
instrument
Data variable
INST C
calibrations
installations
INSTALLATION D
CAL D
10
From day 1 until the end of the cruise, the variable PPAR_OUTPUT is measured by instrument C (instrument instance C). The instrument was commissioned on date 1 (date_valid_from)
11
Instrument C was installed on date 1 (date_valid_from) in position X, Y, Z.
12
instrument C has a manufacturer calibration D. But it not applied to the data variable PPAR_OUTPUT. Thus there is no attribute ppar_output:calibration
Root group